## Slide 1: Heart Beat Monitor
By: Heatem Shakweer - 900150862

## Slide 2: Overview
An application that calculates RPM of heart beat upon collecting ECG data
Using STM32F103C8 board, AD8323 heart beat sensor, and USB to TTL
ECG data is collected over one minute and used to calculate the RPM.

## Slide 3: Architecture
User inputs commands to set the sampling rate, collect data, and report RPM.
Commands are sent over UART from PC to STM32.
According to the received command the STM32 does the required task then it returns to the state of receiving other commands
When Collect command is received, the STM32 sends over UART to the PC the results and the PC receives them.
They are Plotted and converted to a video drawing the samples showing one minute data using pyserial and matplotlib

## Slide 4: Implementation - Keil
Using CubeMx, we initialize the board UART1, ADC1, TIM1, TIM2
We set TIM1 Prescaler to “7” and count period “49999” to be used in microseconds each tick (clock 8MHZ)
We set TIM1 Prescaler to “7999” and count period “62999” to be used in milliseconds to time for 1 minute
Then we start the Timers using “HAL_TIM_Base_Start()” and enable calibration on ADC1 to improve conversion using “HAL_ADCEx_Calibration_Start()”
Then we enter our infinite loop with our initial state A which makes the code wait to receive a command

## Slide 5: Implementation - Keil
If command received is Sampling command, go to state B, where the sampling rate is parsed from the command and our TIM1 delay is calculated as 1/sampling rate. Then it goes back to state A ready to accept commands
If command received is Collect command, go to state C, where the ADC value is taken, ADC stop, value sent over UART, and after wait time is done, ADC start and get next value. The above is repeated until 1 minute passes using TIM2. After 1 minute, it returns to state A ready to accept commands

## Slide 6: Implementation - Python
Initialise data arrays and parameters for plotting.
Using pyserial, opening a serial instance with the associated TTL
Defining our animate function which will be looped by matplotlib animation to read the values from the UART and update the plotting line
Then The user is prompted to input a command. After validating it, it is sent using ser.write() to the UART to be received by the STM32.
If the Command input is collect, the animation.FuncAnimation() is called to read the values.*
*Unfortunetly, there is an issue with the animation function in jupyter it does not show it is converted to a video and the video is displayed after runtime.
*Also due to limited frames, Even though data is all collected in the first 1 minute, it takes up to 6 minutes for the animation function to finish and video produced.

## Slide 7: RPM Calculation
Attempted using heartpy library which takes the data as an array and process it to display RPM and other measures.
However all measures are only showing as nans.

## Slide 8
Thank You